## Slide 1
Rotating machines
Faraday’s Law: Changing magnetic flux through a coil generates voltage
->
->armature winding is stationary and is called the stator
AC machines:
DC machines:
->
rotates and is called the rotor
Armature winding
A synchronous electric motor is an AC motor in which, at steady state,
[1] the rotation of the shaft is synchronized with the frequency of the supply
current; the rotation period is exactly equal to an integral number of AC cycles.
One of the most common electrical motor used in most applications which is known as induction motor.
This motor is also called as asynchronous motor because it runs at a speed less than its synchronous speed.

## Slide 2: Generator activity
With magnets attached, spin rotor
Measure voltage with multi-meter
  Using commutator
  Using slip rings
What’s the difference?
What happened when you change the direction of spin?

## Slide 3
Stator
Rotor

## Slide 4
has DC current which produces the main operating flux
:
,
:
on rotor
:
on stator
:
Flux in armatures produce eddy currents, which can adversely affect the machine
The shown laminations reduce eddy currents

## Slide 5: Generator activity
Replace the magnets with field windings. Connect the two windings in series with a 4 V battery across the windings. Touch the metal with an something sense the magnetism.
Repeat the previous generator activity quickly because the wires heat up!

## Slide 7
Field windings act like a bar magnet (two-pole magnet)
Direct current supplied through stationary brushes that contact rotating slip rings
Rotor: low-powered field winding
Stator: high-powered armature winding

## Slide 8: Generator activity
How does our generator/motor differ from the simple synchronous generator/motor of the previous slide?

## Slide 9
One voltage cycle is generated by one turn of the rotor. Therefore the voltage is synchronous with the rotor—frequency of the voltage (cycles/s=rotor speed rev/s)
60 Hz=3600 RPM

## Slide 10
2 voltage cycles per spin
60 Hz: rotor spins 1800 rpm

## Slide 11
Virtual Power Laboratory
DC Generator Foundation
DC Motor Foundation
DC Generator Construction
DC Motor Construction
DC Generator Experiment
DC Motor Experiment

## Slide 12
10-100 Motor-Generator
Build the 2-pole DC motor as described in the manual. Use the permanent magnets
Take a picture of your motor and in paint, label the armature, stator, commutator, and brushes
Connect 2V across the brushes to turn the motor on.
With your phone, take a ~2s movie.
View in Windows Media Player with 50% speed and count number of turns per second.
Connect 4V across the brushes
Repeat 4-5 using 4V. What did you observe?
Now replace the permanent magnets with an electromagnet
Build a series motor using the connections shown in diagram 5 of page 3 and repeat 3.
Repeat 9 using a shunt motor (diagram 6 on page 4) and repeat 3.
Read pages 1-4 of the manual. You will be quizzed on these. information there.